Basic Electronics
March 20, 2013
Chris K Cockrum
http://cockrum.net

---
Agenda
Agenda
- Goals
- Electricity
- Multimeter Measurements
- Ohms Law
- Watts Law
- LEDs
- LAB

---
Goals
- Understand Voltage, Current, Resistance, and power
- Be able to measure Voltage, Current, and Resistance using a multimeter
- Be able to calculate the value of resistor required to connect an LED to a battery
- Be able to calculate the voltage drop across a resistor in a DC circuit

---
Electricity
- Voltage ( V or E )
  - Difference in potential (charge) between two points
  - Can be though of as analogous to water pressure
  - Unit: Volt
- Current ( I )
  - Amount of electric charge flowing past a point per unit time
  - Can be thought of as analogous to water flow
  - Unit: Ampere (Amp)

---
Electricity
- Resistance ( R )
  - Opposition to the flow of electric current through a component
  - Can be thought of as analogous to water flowing through a pipe (or restriction)
  - Unit: Ohm (Ω)
- Power ( P )
  - Rate of energy transfer from an electric circuit
  - Also defined as the rate of doing work
  - Unit: Watt

---
The Multimeter, Voltage
- Voltage Measurement
  - Set the meter to measure DC Voltage (DCV, 20)
  - Plug the black wire into the COM
  - Plug the red wire into the VΩmA
  - Connect the probes across what you want to measure
- Voltage measurement is minimally intrusive and will usually not affect your circuit

---
Measurement 1 – Battery Voltage
- Set up your meter to measure voltage
- Put the probes across the 9V battery terminals
- You should be reading somewhere near 9V

---
The Multimeter, Resistance
- Resistance Measurement
  - Set the meter to measure Ohms (Ω, 20k [or whatever range is necessary])
  - Plug the black wire into the COM
  - Plug the red wire into the V/ohm/mA
  - Test the meter by touching the probes together – it should read near 0 Ω
  - Connect the probes across what you want to measure
- Resistance measurement should not be performed on a powered circuit

---
Measurement 2 – Resistance
- Set up your meter to measure resistance
- Put the probes across some of the provided resistors
- The resistors should be approximately the value shown on the color code

---
The Multimeter, Current
- Current Measurement
  - Set the meter to measure current (DCA, 20mA)
  - Plug the black wire into the COM
  - Plug the red wire into the V/ohm/mA
  - Connect the probes in series with what you want to measure
- Over-current will blow the fuse in the meter
- The 10A range requires the probe to be connected to the 10A receptacle

---
Measurement 3 – Current
- Set up your meter to measure current (20mA Scale)
- Connect the meter in-line as shown

---
Ohm's Law
E = I x R
- Allows calculation of Voltage (E), Current (I), or Resistance (R)
- Example (Previous measurement):
  - Voltage ( E ) = 9V
  - Resistance ( R ) = 1Kohm
  - 9V = 1Kohm x I
  - I = 9V / 1Kohm = .009 Amps = 9 mA

---
Watt's Law
P = I x E
- Allows calculation of Power (E), Current (I), or Voltage (E)
- Example (Previous measurement):
  - Voltage ( E ) = 9V
  - Current ( I ) = 9mA
  - P = 9mA x 9V = .081 Watts = 81 mW

---
Ohm's and Watt's Laws Combined
E = I x R	P = I x E
P = I x I x R → P = I2R
P = (E/R) x E → P = E2/R
etc.

---
Light Emitting Diodes (LEDs)
- A diode is a component that passes current in one direction better than in the other
- An LED is a type of diode that emits light
- Must be connected with the correct polarity
- Requires a resistor to limit the current

---
Light Emitting Diodes (LEDs)
- Example
  - RED LED, 10mA Max, 2V
  - Battery = 9V
  - E = I x R → R = E / I =
    (9V-2V) / 10mA = 700 ohms
  - Try 1000 ohms:
    - I = E / R = 7V / 1000 = 7mA (close enough)

---
Light Emitting Diodes (LEDs)

---
Light Emitting Diodes (LEDs)

---
Light Emitting Diodes (LEDs)

---
Light Emitting Diodes (LEDs)

---
Resistors in Series and Parallel
- RT = R1 + R2 = 800
- RT = 1 / (1/R3 + 1/R4) = 193.88